## Slide 1
Experimental Setup
Coherence measurements with double pinholes at FLASH2
T. Wodzinski1,2, M. Ruiz-Lopez2 , M. Mehrjoo2, B. Keitel2, M. Kuhlmann2, M. Brachmanski2, S. Künzel1, M. Fajardo1 and E. Plönjes-Palm2
1Group of Lasers and Plasmas (GoLP)
Instituto de Plasmas e Fusão Nuclear (IPFN)
Instituto Superior Técnico Lisboa (IST)
thomas.wodzinski@tecnico.ulisboa.pt
/ DESY
DESY wave front sensor
Adjustable focus (nominal 2m behind first mirror)
Online analysis with DESY WFS (Backpropagation, Zernike Aberrations)
Pinholes of 10 um diameter
Pinholes-B: Variable beam size with KAOS
  6 m from CCD
  107 um to 1570 um separations
Measured beam position with fluorescent coating
Measured pinhole diameters and separations under microscope
KAOS: Variable micro-focus
KB focusing system using bendable mirrors
Exp
FEL
diff. pumping stage
+ WFS diagnostics
+ laser in-coupling
Kirkpatrick-Baez mirror optics
pre-mirror
In = focused
Out = unfocused
Bendable mirrors of 400 mm length with 2° grazing incidence
3.1 µm * 3.3 µm FWHM focus at 8 nm
 up to 5*1016 W/cm2
Beamtime in Nov/Dez 2017 at FL24
Direct coherence measurements with double pinholes & slits
Wave front measurements
PMMA imprints (in collaboration with Chalupsky et al (FZU Prague) & Dziarzhytski (DESY)
Wavelengths 8.0nm, 13.5nm and 18.0nm and different undulator settings
Collaboration of FLASH with M. Zandrando, L. Raimondi et al., Fermi@Elettra
Double Pinholes
2DESY, FLASH
FWHM=(2.1 x 1.7)mm
FWHM=(2.1 x 2.0)mm
FWHM=(2.4 x 2.4)mm
Coherence length vs. Pinhole Separation
Interference pattern example
Measured partially coherent interference pattern (blue) with the reconstructed fully coherent pattern (red) after applying a blind deconvolution algorithm
Simulated intensity distribution from a double-pinhole experiment for different pinhole separations. A divergent beam illuminates the pinholes and the diffracted light propagates in the intermediate zone.
The partially coherent interference pattern is the convolution of a fully coherent pattern with the Fourier-transform of the coherence function g (Clark et al. 2012):
blind-deconvolution
Backpropagation to pinhole plate
The transverse coherence length x is the rms width of the coherence function g:
Simulation of interference in the intermediate zone
rms width
Singer (2013)
In a classical approach, the pinholes would be destroyed by being placed 1.5mm from the focussed beam (Singer 2013).
Here, the double-pinholes were positioned 1m behind the focus. This introduced a curvature to the beam, leading to a diffraction pattern in the intermediate zone instead of the far-field. Usually, one would determine the complex degree of coherence g from the central visibility of the pattern.
The blind-deconvolution method (Clark 2012) can be used here to obtain the coherence length x.
8nm
13.5nm
18nm
This project has received funding from the European Union’s Horizon 2020 Research and Innovation programme under Grant Agreement No 730872.

## Slide 2
Blind-deconvolution method for an interference pattern in the intermediate zone